## Slide 1: Pedaling Forward: The Evolution of Bicycling Infrastructure in 3 Canadian Cities from 2010 to 2022
Richard Wen
Postdoctoral Fellow
Dalla Lana School of Public Health
University of Toronto
richard.wen@utoronto.ca
CARSP Conference 2024
Ottawa, Ontario
June 16-19, 2024
Session1 B: Cyclist Safety

## Slide 2: Cycling … Healthy, but Dangerous?
Improved Fitness & Mental Health
Cleaner Air
Reduced Traffic & Noise
Longer Lives
Teschke, K., Reynolds, C. C., Ries, F. J., Gouge, B., & Winters, M. (2012). Bicycling: Health risk or benefit. UBC Med J, 3(2), 6-11.
Higher Risk of Injury & Death
e.g. 2.3X injury, 1.8X death versus
vehicles in US (1999-2003)
Pollution Exposure
Shorter Lives

## Slide 3: The Pandemic Cycling Boom and Safer Streets
Buehler, R., & Pucher, J. (2022). Cycling through the COVID-19 pandemic to a more sustainable transport future: Evidence from case studies of 14 large bicycle-friendly cities in Europe and North America. Sustainability, 14(12), 7293.
More Cyclists
11 of 13 Countries
(e.g. +27% Italy)
Reduced Speed Limits
30 km/h
(e.g. Slow streets Vancouver)
Cycling Education
Free Courses
(e.g. 6/7th grade schools Vancouver)
More Infrastructure
Network Expansions
(e.g. 17 routes by 2027 Montréal)

## Slide 4: Infrastructure: Is it Happening? How Do We Know?
Accuracy?
Consistency?
Updates?
Top to bottom: https://opendata.vancouver.ca | https://data.calgary.ca | https://open.toronto.ca

## Slide 5: Research Objectives
(2) Evaluate yearly trends in cycling infrastructure across cities
(1) Verify that city installation and upgrade data are accurate
For dedicated cycling infrastructure (painted lanes, buffered lanes, and cycle tracks as defined by the Canadian Bikeway Comfort and Safety (Can-BICS) classification system) in the cities of Vancouver, Calgary, and Toronto from 2010 to 2022:
Winters, M., Zanotto, M., & Butler, G. (2020). At-a-glance-The Canadian Bikeway Comfort and Safety (Can-BICS) Classification System: a common naming convention for cycling infrastructure. Health promotion and chronic disease prevention in Canada: research, policy and practice, 40(9), 288.

## Slide 6: Data
Vancouver Bikeways
opendata.vancouver.ca
Calgary Bikeways
data.calgary.ca
Toronto Bikeways
open.toronto.ca
3666 Road Segments
Local Street bikeways, protected bike lanes, painted lanes, shared lanes
Filter: On-street painted lanes, protected bike lanes, local street bikeways
4169 Road Segments
Cycle tracks, bike lanes, on-street bikeways, shared lanes, temporary and decommissioned routes
Filter: Active bike lanes, cycle tracks
1323 Road Segments
Cycle tracks, bike lanes, neighborhood routes with sharrows, multi-use trails, signed cycling routes
Filter: Cycle tracks, bike lanes

## Slide 7: Methods: Verification

## Slide 8: Methods: Evaluation
Adjusted Yearly Road Lengths
Yearly Road Lengths

## Slide 9: Results: Segment Inclusions and Exclusions

## Slide 10: Results: Installation Year Accuracy, Vancouver
83.3% Correct
97.2% ±1 Year

## Slide 11: Results: Installation Year Accuracy, Calgary
42.1% Correct
62.7% ±1 Year

## Slide 12: Results: Installation Year Accuracy, Toronto
74.5% Correct
78.2% ±1 Year

## Slide 13: Results: Infrastructure per 1000 km of Roadway

## Slide 14: Results: Net Change per 1000 km of Roadway

## Slide 15: Results: Changes Since January 2020, Vancouver

## Slide 16: Results: Changes Since January 2020, Calgary

## Slide 17: Results: Changes Since January 2020, Toronto

## Slide 18: Discussion
Comparability
Standardized infrastructure types across cities
Verified Change Data
Cycling data with confirmed changes and evidence
Strict Exclusions
Temporary/mixed infrastructure & directionality not considered
Potential Data Gaps
Possibly incomplete data for 2022 as cities may not update by end of year
Advantages
Limitations

## Slide 19: Summary
Cycling infrastructure growth since 2009 especially after 2019
~42/74/83% of Calgary/Toronto/Vancouver city data had correct install years.
Verification data important for accurate representation of infrastructure.
Trends comparable across cities with standardized infrastructure types. However, care needed to include appropriate types for purpose of study.

## Slide 20: Thank You for Your Time! Richard Wen Postdoctoral Fellow richard.wen@utoronto.ca R Code and Data for Figures and Tables
https://rrwen.github.io/recovr-infracycle